## Slide 1
Order-Based Planning System
Intelligent Manufacturing Scheduling using Genetic Algorithm Optimization
PrecisionParts Ltd. — Automotive Components Manufacturer
Slide 1 of 11

## Slide 2
The Business Problem
What challenge does Order-Based Planning solve?
❝ Given limited machines and materials, which orders do we produce this week — and what do we delay to minimize total penalty cost? ❞
⚠
Capacity Overload
Multiple orders compete for the same CNC machine or assembly bay in the same week
📦
Material Shortages
Steel rods or rubber seals run out mid-week; some orders can't be fulfilled on time
📅
Promise Date Conflicts
10 orders all promise delivery on May 16 — physically impossible to honour all
💸
Penalty Blind Spots
Delaying a VIP customer (Toyota) costs 10× more than delaying a low-priority garage
→ Manual spreadsheet planning misses interactions between orders, capacity and components.
Slide 2 of 11

## Slide 3
Meet PrecisionParts Ltd.
Our example: an automotive components manufacturer
🏭
PrecisionParts Ltd. manufactures Engine Blocks, Brake Assemblies, and Exhaust Pipes for OEM customers. They receive ~30 orders per month across 3 factory locations.
🔧 Products
What they manufacture
Engine Block V6 — $1,200
Brake Assembly — $340
Exhaust Pipe — $180
🏢 Customers
Who they sell to
Toyota → VIP priority
Ford → High priority
Local Garages → Low priority
📍 Locations
Where they produce
Plant A — Detroit (USA)
Plant B — Stuttgart (DE)
Plant C — Chennai (IN)
Slide 3 of 11

## Slide 4
The 6 Building Blocks
Master data that drives the planning engine
📦
Products
What is being manufactured (code, name, price, lead time)
🏢
Customers
Who ordered it (priority: VIP / High / Low)
⚙
Restrictions
Production resources with weekly capacity (CNC Line, Assembly Bay, Paint Shop)
🔩
Components
Raw materials with weekly availability (Steel Rods, Rubber Seals, Bolts)
📋
Sales Orders
Customer orders with promise dates, linked to restrictions + components
💸
Penalty Rules
Cost per day of delay per customer priority (VIP: $500/day, High: $200/day)
Slide 4 of 11

## Slide 5
Anatomy of a Sales Order
How a single order connects to resources and materials
📋 SO-0001 — Toyota
Product: Engine Block V6
Quantity: 50 units
Promise: 16 May 2025
Priority: VIP
Penalty: $500 / day late
⚙ Restrictions Used
CNC Machine Line A
3 hrs / unit → 150 hrs total
Assembly Bay
1.5 hrs / unit → 75 hrs total
🔩 Components Used
Steel Rods
2 per unit → 100 rods total
Aluminum Sheet
1 per unit → 50 sheets total
Fastener Kit
4 per unit → 200 kits total
Each order explicitly declares which machines it occupies and which materials it consumes. The optimizer uses this to calculate weekly load across all orders simultaneously.
Slide 5 of 11

## Slide 6
The Optimization Engine
Genetic Algorithm — finds the lowest-penalty schedule
For each sales order: should we process it ON its promise date, or push it out 1, 2 … 8 weeks to relieve congestion?
1
Encode
Each candidate schedule = a 'chromosome' {SO-0001: delay 0wk, SO-0002: delay 1wk, …}
2
Evaluate
Fitness = total penalty cost (late delivery + capacity overrun + shortage)
3
Select
Lower-cost schedules survive Tournament selection across 50 candidates
4
Crossover
Combine two good schedules to produce a better child schedule
5
Mutate
Randomly shift one order's week to escape local optima
6
Repeat
Evolve for 100 generations Return the best schedule found
Slide 6 of 11

## Slide 7
How Penalty Cost is Calculated
The fitness function the algorithm minimises
💸
Late Delivery
Per order delayed past promise date
Delay days × penalty rate per day
VIP customer: $500/day late
High priority: $200/day
Low priority: $50/day
Example: Toyota SO-0001 delayed 7 days = $3,500
⚙
Capacity Overrun
When a machine is over-booked in a week
Over-usage × penalty_cost_per_unit
Soft: capacity > 0 → linear penalty
Hard: capacity = 0 → ×1,000,000,000 penalty
Order marked INFEASIBLE
Example: CNC +40 hrs × $500 = $20,000
🔩
Component Shortage
When stock is insufficient for a week
Shortage units × unit_cost × 3
Soft: some stock → 3× cost multiplier
Hard: zero stock → ×1,000,000,000 penalty
Order marked INFEASIBLE
Example: 30 rods short × $45 × 3 = $4,050
Slide 7 of 11

## Slide 8
Optimization Results Dashboard
What the planner sees after running the algorithm
70%
On-Time Delivery
7 / 10
Orders On Time
4.2 d
Avg Delay
$18,400
Total Penalty
2
Capacity Violations
1
Component Shortages
📋 Order Results
Per-order table: original vs optimised date, delay days, penalty, feasibility. Click any row to see components & restrictions used.
⚙ Capacity Analysis
Heat map of weekly machine utilisation. Red = over capacity. Drill into each restriction.
🔩 Component Analysis
Weekly stock vs demand chart. Shortage weeks highlighted. Sorted by demand ratio.
🚨 Constraint Summary
All violations ranked by cost. Capacity + component + late orders in one view.
Slide 8 of 11

## Slide 9
Order Results — Sample Output
Each row shows what changed for a sales order; click for full detail
Order #
Customer
Product
Priority
Original
Optimised
Delay
Penalty
Status
SO-0001
Toyota
Engine Block V6
VIP
16 May
16 May
✓ 0d
$0
✓ On Time
SO-0002
Ford
Brake Assembly
High
16 May
23 May
+7d
$1,400
Delayed
SO-0003
Local Garage
Exhaust Pipe
Low
23 May
23 May
✓ 0d
$0
✓ On Time
SO-0004
Toyota
Brake Assembly
VIP
23 May
30 May
+7d
$3,500
Delayed
SO-0005
Ford
Exhaust Pipe
High
30 May
30 May
✓ 0d
$0
✓ On Time
🖱 Click any row → modal shows Components Used, Restrictions Used, and Date of Processing
Order SO-0001 ×
Customer: Toyota | Product: Engine Block V6 | Priority: VIP | Qty: 50
Date of Processing: 16 May 2025
⚙ Restrictions: CNC Line A (3 hrs/unit), Assembly Bay (1.5 hrs/unit)
🔩 Components: Steel Rods (2/unit), Aluminum Sheet (1/unit), Fastener Kit (4/unit)
Slide 9 of 11

## Slide 10
Capacity & Component Analysis
Visual drill-down into machine load and material stock
⚙ Capacity Heat Map — CNC Machine Line A
48%
W18
72%
W19
132%
W20
85%
W21
55%
W22
41%
W23
■ <60% OK ■ 60-80% Moderate ■ 80-100% High ■ >100% Violation
⚠ Week 20 Violation Detail
Capacity Available: 200 hrs
Required: 264 hrs
Over-capacity: +64 hrs
Violation Cost: $32,000
→ Solution: optimizer delayed SO-0002 by 1 week
🔩 Component Analysis — Steel Rods
Week
Available
Required
Shortage
Status
W18
500
320
✓ 0
✓ OK
W19
400
380
✓ 0
✓ OK
W20
200
340
✗ 140
Shortage
W21
600
280
✓ 0
✓ OK
W22
350
210
✓ 0
✓ OK
Week 20 shortage (140 rods) caused orders using Steel Rods to shift to Week 21 where 600 units are available.
Slide 10 of 11

## Slide 11
Business Value & Summary
From guesswork to an optimised, defensible production schedule
⚡
Speed
Schedule 30 orders in seconds where manual planning takes hours
🎯
Accuracy
Simultaneously respects machines, materials AND customer priorities
💡
Transparency
Every delay explained with exact penalty cost breakdown
📤
Actionability
Excel export ready for shop floor and ERP upload
How it works — end to end
Enter Orders
→
Set Machine Capacities
→
Define Material Availability
→
Run Optimization
→
Review Results
→
Export Schedule
"Given our real constraints — what is the best possible delivery schedule, and what does the unavoidable cost look like?"
Slide 11 of 11